# SPECIFICATIONS FOR MEP – 16

| 1. | ITEM | PULSE VALVE WITH INTEGRAL SOLENOID VALVE |
| --- | --- | --- |
| 2. | APPLICATION | TO CLEAN THE BAGS BY PULSING THE COMPRESSED AIR 2 TO 7 Kg/cm² |
| 3. | VALVE CONSTRUCTION |  |
|  | 3.1 FORM OF FLOW | 2/2 NORMALLY CLOSED |
|  | 3.2 MATERIAL OF CONSTRUCTION |  |
|  | 3.2.1 VALVE BODY | DIE CAST ALUMINIUM |
|  | 3.2.2 VALVE SEATS/DIAPHRAGM | IMPORTED POLYESTER |
|  | 3.3 SIZES |  |
|  | 3.3.1 SIDE CONNECTIONS | ¾ ” BSP FEMALE |
|  | 3.3.2 ORIFICE | 25 mm |
|  | 3.3.3 KV FACTOR | 11 |
| 4 | APPLICATION DATA |  |
|  | 4.1 FLUID (MEDIUM) CONTROLLED | DRY COMPRESSED AIR |
|  | 4.2 ADDITIVES ETC. | NOT APPLICABLE |
|  | 4.3 FLUID (MEDIUM) TEMPERATURE | MAXIMUM TEMPERATURE 65ºC |
|  | 4.4 OPERATING PRESSURE | 2 TO 7 Kg |
|  | 4.5 AMBIENT TEMP. | 55ºC |
| 5 | ELECTRICAL DATA |  |
|  | 5.1 VOLTAGE | 230V/110V , 50 Hz ±10% |
|  |  | 24VDC, -5% +20% |
|  | 5.2 COIL CONSTRUCTION | MOULDED |
|  | 5.3 COIL CLASS | CLASS-F |
|  | 5.4 DUTY | ON-OFF DUTY ON TIME : 20 TO 200 MILISEC (ADJUSTABLE) OFF TIME : 2 TO 60 SEC (ADJUSTABLE ) |
|  | 5.5 POWER CONSUMPTION | 19 VA (for 230V and 110V) |
|  |  | 20 W (for 24VDC) |
| 6 | GENERAL DATA |  |
|  | 6.1 FREQUENCY OF OPERATION | CONTINUOUS WITH ON-OFF DUTY AS PER DUTY CONDITIONS MENTIONED ABOVE |
|  | 6.2 TYPE OF PROTECTION | COIL CONNECTOR -IP 65 |
|  | 6.3 CABLE ENTRY | PG – 9 TYPE |
|  | 6.4 MOUNTING POSITION | SUITABLE FOR ANY POSITION |
| 7 | MAKE | MANIKS |
| 8 | MODEL NO. | MEP16 |